Caledonian

Fire Resistant Optic Fiber Cables

www.caledonian-tech.net	www.caledonian-tech.com

Fire resistant Central Loose Tube Fiber Optic cables

Application

These cables are characterized by light weight and small diameter, suitable for both aerial and duct installation. They are mainly installed inside buildings, tunnels,subways or closed areas in general, specially designed to guarantee the signal transmission even in case of fire. The cable can also be used for direct burial for armoured version.

Standards

Basic design to Telcordia GR-20 / RUS 7 CFR 1755.900 (REA PE-90) / ICEA S 87-640

FIRE PERFORMANCE

|  | IEC 60331-25; BS 6387 CWZ; DIN VDE 0472-814(FE180); |  |
| --- | --- | --- |
| Circuit Integrity | CEI 20-36/2-1; SS229-1; NBN C 30-004 (cat. F3); |  |
|  | NF C32-070-2.3(CR1) |  |
| System circuit integrity | DIN 4102-12, E30 depending on lay system |  |
| Flame Retardance (Single Vertical | EN 60332-1-2; IEC 60332-1-2; BS EN 60332-1-2; VDE |  |
| Wire Test) | 0482-332-1 ; NBN C 30-004 (cat. F1); NF C32-070-2.1(C2); |  |
|  | CEI 20-35/1-2; EN 50265-2-1*; DIN VDE 0482-265-2-1* |  |
| Reduced Fire Propagation | EN 60332-3-24 (cat. C); IEC 60332-3-24; BS EN 60332-3-24; |  |
| (Vertically-mounted bundled wires | VDE 0482-332-3; NBN C 30-004 (cat. F2); NF C32-070-2.2(C1); |  |
| & cable test) | CEI 20-22/3-4; EN 50266-2-4*; DIN VDE 0482-266-2-4 |  |
| Halogen Free | IEC 60754-1; EN 50267-2-1; DIN VDE 0482-267-2-1; |  |
|  | CEI 20-37/2-1 ; BS 6425-1* |  |
| No Corrosive Gas Emission | IEC 60754-2; EN 50267-2-2; DIN VDE 0482-267-2-2; |  |
|  | CEI 20-37/2-2 ; BS 6425-2* |  |
| Minimum Smoke Emission | IEC 61034-1&2; EN 61034 -1&2; DIN VDE 0482-1034-1&2; |  |
|  | CEI 20-37/3-1&2; EN 50268-1&2*; BS 7622-1&2* |  |
| No Toxic gases | NES 02-713; NF C 20-454 |  |
| Note: Asterisk * denotes superseded standard. |  |

CABLE CONSTRUCTION

Fibers: Singlemode and multimode fibers, with loose tube technology.

Structure: Central loose tube cable contains one tube with 2-24 single or multimode fibers, which are filled with water blocking gel.

Fire barrier: The jelly filled tube with up to 24 fibers is wrapped with a fire blocking mica glass tapes. Water blocking: The jelly filled tube is waterblocked by using swellable tape and thread.

Reinforcement: Either aramid yarn or fiber glass is wound around the tube to provide physical protection and tensile strength, with added fire protection.

Inner sheath (optional): The cable can be jacketed with either PE or thermoplastic LSZH inner sheath. PE is the preferred option in outdoor environment for water protection purpose.

Moisture Barrier Tape (optional): An aluminum moisture tape can be incorporated under the sheath for water blocking and shielding purpose.

ADDISON   135

ADDISON

Armouring(optional):

For diect burial, either galvanized steel wire braid, corrugated steel tape armour or galvanized steel wire armour is applied over an inner polyethylene or LSZH sheath. For steel tape armour, the

0.15mm thick steel tape is coated with a copolymer and applied with an overlap. For steel wire braid or armour, single layer of galvanized steel wire braid or armour is applied.

Ripcord (optional): An optional ripcord can be located under the jacket to facilitate jacket removal.

Outer Sheath: Thermoplastic LSZH compound type LTS3 as per BS 7655-6.1(Thermosetting LSZH compound type SW2-SW4 as per BS 7655-2.6 can be offered.)

Fiber colour code

| Fiber colour code | 1 | Red | 7 | Brown |
| --- | --- | --- | --- | --- |
|  | 2 | Green | 8 | Violet |
|  | 3 | Blue | 9 | Turquoise |
|  | 4 | Yellow | 10 | Black |
|  | 5 | White | 11 | Orange |
|  | 6 | Grey | 12 | Pink |

CONSTRUCTION

Unarmoured type

CONSTRUCTION PARAMETERS

|  | Fiber | Tube | Nominal | Approx. |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Cable Code |  |  | Overall |  | Tension load | Crush |  |
|  | Count | Diameter |  | Weight |  |  |  |
|  |  |  | Diameter |  |  |  |  |
|  | (n°) | mm | mm | kg/km | N | N/100mm |  |
| CLA-B-C-H-J-FR | 02-06 | 2.7 | 8.0 | 70 | 1000 | 1500 |  |
| CLA-B-C-H-J-FR | 08-16 | 3.5 | 9.0 | 90 | 1200 | 1500 |  |
| CLA-B-C-H-J-FR | 18-24 | 4.2 | 10.0 | 100 | 1500 | 1500 |  |

136	Caledonian   sales@caledonian-cables.net   uk@caledonian-cables.net

Caledonian

Fire Resistant Optic Fiber Cables

www.caledonian-tech.net	www.caledonian-tech.com

Steel Wire Braid

|  |  |  |  | Fiber |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | Jelly Filled Central Loose Tube |  |  |
|  |  |  |  | Mica Glass Tape |  |  |
|  |  |  |  | Water -blocking Tape(optional) |  |  |
|  |  |  |  | Aramid Yarn/Fiber Glass Yarn |  |  |
|  |  |  |  | PE/LSZH Inner Sheath(optional) |  |  |
|  |  |  |  | Ripcord(optional) |  |  |
|  |  |  |  | Aluminum Moisture Barrier(optional) |  |  |
|  |  |  |  | Steel Wire Braid |  |  |
|  |  |  |  | LSZH Outer Sheath |  |  |
| CONSTRUCTION PARAMETERS |  |  |  |  |  |  |
|  | Fiber | Tube | Nominal | Approx. |  |  |  |  |
| Cable Code |  |  | Overall |  | Tension load |  | Crush |  |
|  | Count | Diameter |  | Weight |  |  |  |  |
|  |  |  | Diameter |  |  |  |  |  |
|  | (n°) | mm | mm | kg/km | N |  | N/100mm |  |
| CLA-B-C-2Y(SWB)H-J-FR | 02-06 | 2.7 | 11.5 | 160 | 1000 |  | 2000 |  |
| CLA-B-C-2Y(SWB)H-J-FR | 08-16 | 3.5 | 12.0 | 180 | 1200 |  | 2000 |  |
| CLA-B-C-2Y(SWB)H-J-FR | 18-24 | 4.2 | 13.0 | 200 | 1500 |  | 2000 |  |

Corrugated Steel Tape Armour

Fiber

Jelly Filled Central Loose Tube

Water -blocking Tape(optional)

Mica Glass Tape

Aramid Yarn/Fiber Glass Yarn

Aluminum Moisture Barrier Tape(optional)

Ripcord(optional)

PE/LSZH Inner Sheath(optional)

Corrugated Steel Tape Armour

LSZH Outer Sheath

CONSTRUCTION PARAMETERS

| Cable Code | Fiber | Tube | Diameter | Approx. | Tension | Crush |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Count | Diameter |  | Weight | load |  |  |
|  | (n°) | mm | mm | kg/km | N | N/100mm |  |
| CLA-B-C-2Y(STA)H-J-FR | 02-06 | 2.7 | 13.0 | 200 | 1000 | 2500 |  |
| CLA-B-C-2Y(STA)H-J-FR | 08-16 | 3.5 | 14.0 | 220 | 1200 | 2500 |  |
| CLA-B-C-2Y(STA)H-J-FR | 18-24 | 4.2 | 14.5 | 250 | 1500 | 2500 |  |

ADDISON   137

ADDISON

Steel Wire armour

CONSTRUCTION PARAMETERS

|  | Fiber | Tube | Nominal | Approx. | Tension |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Cable Code |  |  | Overall |  |  | Crush |  |
|  | Count | Diameter |  | Weight | load |  |  |
|  |  |  | Diameter |  |  |  |  |
|  | (n°) | mm | mm | kg/km | N | N/100mm |  |
| CLA-B-C-2Y(SWA)H-J-FR | 02-12 | 2.7 | 10.5 | 180 | 2500 | 4000 |  |
| CLA-B-C-2Y(SWA)H-J-FR | 16-24 | 3.5 | 11.0 | 210 | 2500 | 4000 |  |

Physical AND THERMAL PROPERTIES

Temperature range during operation (fixed state):-20°C - +60°C

Temperature range during installation (mobile state): 0°C - +50°C

Minimum operation Bending Radius: 10 times the outer diameter for unarmoured cables 20 times the outer diameter for armoured cables

Minimum Installation Bending Radius: 20 times the outer diameter

mechanical PROPERTIES

| Maximum Compressive Load | 4000N for unarmoured cables |  |
| --- | --- | --- |
|  | 5000N for armoured cables |  |
| Repeated Impact: | 4.4 N.m (J) |  |
| Twist (Torsion): | 180×10 times, 125×OD |  |
| Cyclic Flexing: | 25 cycles for armoured cables; |  |
|  | 100 cycles for unarmoured cables. |  |
| Crush Resistance: | 263N/cm (150lb/in) |  |
| Fiber Compliance |  |  |
| Temperature Cycling | IEC60794-1-2-F2 |  |
| Tensile Strength | IEC60794-1-2-E1A |  |

138	Caledonian   sales@caledonian-cables.net   uk@caledonian-cables.net

Caledonian

Fire Resistant Optic Fiber Cables

www.caledonian-tech.net	www.caledonian-tech.com

| Crush | IEC60794-1-2-E3 |
| --- | --- |
| Impact | IEC60794-1-2-E4 |
| Repeated Bending | IEC60794-1-2-E6 |
| Torsion | IEC60794-1-2-E7 |
| Kink | IEC60794-1-2-E10 |
| Cable Bend | IEC60794-1-2-E11 |
| Cool Bend | IEC60794-1-2-E11 |

TYPE CODES

CLA-B-C-D-E-F-G-FR

FR: Fire Resisting

Water blocking gel in tubes

X: No water-blocking J: Water blocking gel between jackets; D: Dry water-blocking between cable jackets

Outer Sheath

2Y: PE

Y: PVC

H: LSZH

Armour

Blank: No armour

STA: Corrugated steel tape armour

SWA: Steel wire armour

SWB: Steel wire braid

Inner Sheath

2Y: PE

Y: PVC

H: LSZH

C No of Fibers B Fiber Type

- 50/125 um(OM3) 7: NZDS SM fiber per ITU-T G.656

- 50/125 um(OM2) 8: NZDS SM fiber per ITU-T G.655

- 62.5/125um(OM1) 9: Standard SM fiber per ITU-T G.652.D

Tube Diameter

A: 2.7mm

B: 3.5mm

C: 4.2mm

GR-20/RUS 7 CFR1755N.900 (REA PE-90)

Standard

ICEANS87-640

W	E

|  |  |  |  | Circuit Integrity | Reduced Fire Propagation | Flame Retardancy |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | NF C32-070-2.2(C1) | NF C32-070-2.1(C2) |  |
|  | Standard | IEC 60331/BS 6387 |  |  |  |
|  |  |  | NF C32-070-2.3(CR1) IEC60332-3-24/EN50266-2-4 | IEC60332-1-2/EN50265-2-1 |  |
|  |  |  |  |  |  |  |  |  |  |  |  | Zero |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | W | E |  |  |

|  |  |  | Low Corrosivity | Low Smoke Emission |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Halogen Free |  |  |
|  | Low Toxicity | IEC60754-2 | IEC 61034-1&2 | IEC60754-1 | Functional Integrity |  |
|  |  | EN50267-2-2/3 |  |  |  |  |
| NES 02-713/NF C 20-454 | NF C 32-074 | EN 50268-1&2/NF C32-073 | EN50267-2-1 | DIN 4102-12 |  |

ADDISON   139