Date: 13 Feb. 2012

Part No.: PC80513

Flame Retardant Cable to IEC60332-3C

300/500V 2C/ 4C/ 8C 0.5 mm2 Flexible Cu/LSZH/TCWB/LSZH

Application

The cables are mainly used in power stations, mass transit underground passenger systems, airports, petrochemical plants, hotels, hospitals, and high-rise buildings.

Construction

Conductor:   	 	Stranded flexible copper wire conductor

Insulation:  	 	LSZH

Core Identification:

Color coding as per DIN47100

Shield:     		Overall tinned copper braid

Sheathing:     		LSZH

Sheath Color:  	Light grey

Packing:           		The cables are delivered on non-returnable wooden drums.

Technical data

| No. of Core | Conductor Size and Stranding | Nom. Thickness of Insulation | Tinned Copper Wire Braided Cable |
| --- | --- | --- | --- |
|  |  |  | Nominal Thickness of Sheath | Nominal Overall Diameter | Approx. Weight |
| No. | mm2 | mm | mm | mm | kg/km |
| 2 | 0.5 mm2 (16/0.2mm) | 0.45 | 1.0 | 6.3 | 62 |
| 4 | 0.5 mm2 (16/0.2mm) | 0.45 | 1.0 | 7.2 | 88 |
| 8 | 0.5 mm2 (16/0.2mm) | 0.45 | 1.0 | 8.9 | 135 |

Physical characteristics                                          Temperature rating:

- During operation: -20 to + 90℃

- During Installation: 0 to + 90℃

Minimum bending radius:

During installation: 3 x Overall Diameter

Flexibility: 	Flexible

Electrical characteristics

Rated voltage:                         	300/500V

Max. conductor resistance at 20ºC:      	39 ohm/km

Min insulation resistance:               	≥500 M Ohm×Km

Test voltage:                            	2000V

# Text boxes

Overall Tinned Copper Braid

LSZH Outer Jacket

LSZH Insulation

Flexible Copper Conductor